## Slide 1: Wings Navigation Exercises
Tips and Tricks
Notes: Introductory slide

## Slide 2: Wings Navigation Exercises
B
BRONZE
≥ 100 nm • ≥ 1 land-away • ≤ 1 day
S
SILVER
≥ 200 nm • ≥ 2 land-aways • ≤ 2 days
G
GOLD
≥ 300 nm • ≥ 3 land-aways • ≤ 3 days
D
DIAMOND
≥ 500 nm • ≥ 5 land-aways • ≤ 5 days
ACCURACY
Total fuel burn
and journey time
within ±20%
1
CHOOSE THE CHALLENGE
Select an award level and overall distance.
Choose a route you would be happy to fly.
Identify possible land-away aerodromes.
2
BUILD THE ROUTE
Add a waypoint at least 20 nm after take-off.
Use features that are easy to identify.
Add planned altitude for every leg.
3
RUN THE NUMBERS
Generate a PLOG for each individual flight.
Transfer distances and times to a spreadsheet.
Estimate hourly fuel burn from PoH or experience.
4
RECORD THE PLAN
Enter planned times, durations and waypoint.
Record planned total fuel and distance.
Give the plan to an observer or submit it.
5
PREPARE & FLY SAFELY
Complete normal pre-flight planning and checks.
Carry plenty of fuel and record start quantity.
Safety always takes priority over the exercise.
6
CAPTURE ACTUALS
Record leaving and joining circuit times.
Record each specified waypoint time.
Log en-route fuel purchases and final fuel.
7
COMPARE & LEARN
Compare planned journey time with actual time.
Compare planned fuel burn with actual fuel.
Adjust assumptions to improve the next plan.
IN-FLIGHT DISCIPLINE
Keep ETA END on target
Use airspeed thoughtfully rather than chasing every wind change.
T
TIME
Actual vs planned
Circuit exits • waypoints • arrivals
F
FUEL
Start + purchases − finish
Include taxi, take-off and landing circuit
S
SAFETY
Always overrides the plan
Weather • aircraft • pilot • fuel margins
Plan accurately • Fly safely • Record evidence • Learn from actuals
PLAN → FLY → IMPROVE

## Slide 3: Criteria for Wings Navigation
Criteria for each level of award:
  Bronze ≥ 100nm flight, ≥ 1 land-away, 1 day
  Silver ≥ 200nm flight, ≥ 2 land-away, ≤ 2 days
  Gold ≥ 300nm flight, ≥ 3 land-away, ≤ 3 days
  Diamond ≥ 500nm flight, ≥ 5 land-away, ≤ 5 days
Plan and execute: total fuel burn within +/- 20%
total journey time within +/- 20%
Fuel burn must allow for taxi / takeoff / circuits / landing
Journey time is just between airfields & waypoints

## Slide 4: Getting started

## Slide 5: Initial plan, no landings yet

## Slide 6: Add in land-aways and times

## Slide 7: Running the numbers
Distances and times taken straight from the PLOG
You can print this out and fill in as you do the flights
Specified waypoints highlighted

## Slide 8: Record the plan
(6) Use the template from the Wings website, fill in the planned times and durations from the spreadsheet (airfields plus the specified waypoint)
(7) Fill in planned total fuel use and total distance
(8) Give to observer or email to wings@bmaa.org

## Slide 9: Executing the flight

## Slide 10: While you’re flying …
Keep an eye on ETA END – adjust airspeed to keep this on target

## Slide 11: Completed plan vs. actuals
Fuel burn wasn’t as high as I predicted
So next time, reduce the planned burn rate and watch the accuracy increase

## Slide 12: Putting it all together